## Slide 1: Embedded AI medical quadcopter
Under supervision of: Dr. Kareem Badawi
Dr. Mahmoud Hamed
Student names: Hend Emad Saber
Nada El-Sayed Hassan
Govani Sami George
Aliaa Magdy Abd Al-Ghany
Hager Ahmed Kotb

## Slide 2
Problem definition
Reference:
[1] Fernández-Ruiz, I. (2021). Drone delivery of defibrillators for sudden cardiac arrest could shorten response times. Nature Reviews Cardiology, 18(11), 740–740. https://doi.org/10.1038/s41569-021-00618-0
According to reference[1], the first drone for out of hospital cardiac arrest was proposed in Dec. 2021.

## Slide 3
System architecture
Quadcopter
Cardiac arrest prediction
Hardware components
Control
Landing image processing
Path planning
CPR

## Slide 4
Cardiac arrest prediction
Path planning
Landing image processing
If someone may have a sudden cardiac arrest at any time
To autonomously go from its initial location to the patient location
To land on the right place for the CPR function

## Slide 5
Cardiac arrest prediction

## Slide 6: Cardiac arrest prediction (Supervised classification problem)
Data collection
Data cleaning
Exploratory data analysis (EDA)
Feature engineering
Modelling
Deployment
Hospitals dataset
Logistic regression
Random Forest
XGBoost
Decision tree
Flask framework

## Slide 7
Data cleaning & EDA
2. Data cleaning
Normality
Balancing
Box-Cox transformation
SMOTE technique
Outliers removing
Correlation
Missing values
Box- Cox transformation: Sakia, R. M. (1992). The box-cox transformation technique: A Review. The Statistician, 41(2), 169. https://doi.org/10.2307/2348250

## Slide 8
5. Modelling
Modelling
Logistic regression
Decision tree
Random forest
XGBoost
With accuracy of
97.5%

## Slide 9
Random Forest algorithm
A tree ensemblele algorithm, based on building a bunch of decision trees and apply voting between their results them to predict the right class (If with high possibility for cardiac arrest or not).
How does this work and how do these decision tress is built?

## Slide 10
Random forest logic
Applying bagging (sampling with replacement technique)Choose random k features which are
Applying bagging (sampling with replacement technique)Choose random k features which are √(█(𝑇ℎ𝑒 𝑡𝑜𝑡𝑎𝑙 𝑛𝑢𝑚𝑏𝑒𝑟 𝑜𝑓 @𝑓𝑒𝑎𝑡𝑢𝑟𝑒𝑠 @𝑖𝑛 𝑡ℎ𝑒 𝑑𝑎𝑡𝑎𝑠𝑒𝑡))
Choose the feature with the maximum reduction in impurity to split the values of the features on.
Apply voting for the total produced decision trees.
Choose the feature with the maximum reduction in impurity to split the values of the features on.
Apply voting for the total produced decision trees.
When does creating the decision trees stop?
1. When decision tree splitting tops when reaching the maximum depth value that is given to the algorithm.
2. Or when the number of decision trees reached maximum which is also given to the algorithm.
The given best hyperparameters values are calculated using cross validation techniques.

## Slide 11
6. Deployment
Using flask framework

## Slide 12
Path planning
References:
[1] Veras, L. G., Medeiros, F. L., & Guimaraes, L. N. (2019). Systematic literature review of sampling process in rapidly-exploring random trees. IEEE Access, 7, 50933–50953. https://doi.org/10.1109/access.2019.2908100
[2] Gugan, G., &amp; Haque, A. (2023). Path planning for autonomous drones: Challenges and future directions. Drones, 7(3), 169. https://doi.org/10.3390/drones70301 69
[3] LaValle, S.M., 1998. Rapidly-exploring random trees: A new tool for path planning.

## Slide 13
Path planning
RRT* Algorithm
Informed RRT* Algorithm
After
optimization
Ellipse sampling technique
Produced the path in 6 seconds
The drone reached the goal of 7m in 22 seconds using SITL Simulation
The drone reached the goal of 7m far from the start in 22 seconds
(6seconds of path calculations and 14 seconds for movement with speed 0.5 m/sec)
Assumption:
GPS locations must be converted into x and y format, this is done using these equations where R = 6371 km

## Slide 14
Path planning using RRTs logic:
After applying the ellipse sampling technique

## Slide 15
Landing image processing

## Slide 16
Landing image processing
(With acuuracy of 100%)

## Slide 17
YOLO algorithm
Produce vector (label)
Using
neural networks
97% 5%
39% 55%
Class probability map

## Slide 18
Classification
Conv2d layer
Max pooling layer
Conv2d layer
Max pooling layer
Dropout layer
Flatten layer
Dense layer
Classification model
Compression
For decreasing the model size to reduce time and power consumption

## Slide 19
Heart Rate monitor watch

## Slide 20: Heart rate monitor watch
overview
A watch is a wearable technology that is designed to monitor the wearer's heart rate in real-time which can be an early warning sign of cardiac arrest.
PURPOSE
In the case of the heart rate sensor detect stopping patient’s heartbeat the watch publishes the patient’s location to the server that can be a valuable tool for helping the drone locate the patient quickly.

## Slide 21: Proposed design
ESP8266
MAX30102 sensor
MAX30102 sensor
OLED Display
Adafruit IO

## Slide 22: MAX30102 Heart Rate and Pulse Oximeter Sensor
The sensor is an I2C-based used as both a heart rate monitor and a pulse oximeter.
Vcc (works on 3.3V )

## Slide 23: How MAX30102 Sensor Works?
Integrates photodetector, RED and IR leds.
using a technique called photoplethysmography (PPG)
As the blood is pumped through the finger with each heartbeat
creating a changing waveform at the output of the photodetector

## Slide 24: Ublox NEO-M8N GPS
It uses the Global Navigation Satellite System (GNSS)
supports UART communication protocol
powered using a 3.3V or 5V
OLED Display
    have an I2C interface

## Slide 25: Adafruit connection
ESP8266
Oled display
If button pressed
Publish Using MQTT
Publish Using MQTT
The sensor sends data

## Slide 26: Drone control

## Slide 27
A Ground Control Station (GCS) is a software used to remotely control and monitor a drone. It provides real-time telemetry data and video footage, allowing the operator to control the drone's flight path and settings.
GCS
MAV LINK

## Slide 28
The project is carried out in several stages, starting with the development of the drone control script and testing it using software in the loop(SITL). The project also involves monitoring the battery health and EKF parameters of the drone and identifying potential barriers or problems that may arise during testing.

## Slide 29
The Rpi4 is then connected to a camera and Xserver to enable QR code landing.
Xming

## Slide 30
Finally, the project is completed by connecting all remaining parts of the project using a server and Bluetooth.
Accessing Watch is achieved using IO server which includes subscribing to the heartbeat data of a patient watch and detecting arrhythmic cases.
Accessing CPR is achieved using Bluetooth, and a message is sent to start its function.
RPI 4
Cloud IO server
Bluetooth

## Slide 31
Add redundant sensors to ensure that the drone can continue flying even if one system
Distribute the processing across multiple boards on the Raspberry Pi 4 to improve performance in case of processing large amount of data or perform complex calculations.
Implement real-time monitoring of critical drone parameters such as battery level, altitude, and speed; to alert you to any potential safety issues. This is done using yocto GUI.
Use backup communication if the primary communication link between the drone and the

## Slide 32: Pixhawk and Drone Connection

## Slide 33
CPR (Cardiopulmonary Resuscitation)

## Slide 34: CPR based on AVR microcontroller
Introduction
CPR is a technique used to maintain blood flow by chest compression when the heart has stopped functioning.
AVR
Bluetooth module
switches
DC Motor
Servo motor

## Slide 35: 1-Servo motor
Used for separating CPR part from drone
PWM signal needed

## Slide 36: 2-DC Motor
Using N20 DC motor for automatic chest compression
Using Darlington with motor as a switch
provides high current gain, allowing it to handle the current requirements of the DC motor.

## Slide 37: 3-Bluetooth module
HC05 Bluetooth module used for wireless communication between AVR microcontroller and Raspberry pi
Communicate with AVR via UART
Operate on 5v and 3.3v

## Slide 38: USART(Universal serial asynchronous Receiver transmitter)
USART connection
Frame format

## Slide 39: 4-Switches using interrupt
Interrupt
Specific interrupt enable
Global interrupt enable
Peripheral interrupt flag
Interrupt controller
Interrupt ID
ON DATA BUS
Processor
Vector table in flash

## Slide 40
If switch1 pressed
Low on INT0 pin
Execute inside ISR0 (rotate servo motor 90)
If switch2 pressed
Low on INT1 pin
Execute inside ISR1 (working or stopping CPR)

## Slide 41: Flowchart
start
Initialize pin direction and values
Initiate Timer1,EXTI0,EXTI1
Read a received data
If data=1
Rotate servo 90 degree then start DC motor
True
If data=2
False
Stop DC motor

## Slide 42: Future plan
The Quadcopter can be used in unknown environment by applying SLAM algorithm and using RPLidar. It also may also include feature extraction algorithm to be able to act in dynamic environment .
Implement real-time monitoring of critical drone parameters such as battery level, altitude, and speed; to alert you to any potential safety issues.
Connect the watch with a smartphone this enable communication features such as calls, text messages, and notifications. This allows users to stay connected without having to reach for their smartphone.
connect sensor to detect whether compressions are being performed correctly and sensor to measure the force of compression.